## Slide 1
Lecture 2
Binary Numbers
Unsigned/Singed number

## Slide 2
Number in a Computer | 
Unsigned integers | Signed integers
Integers have positive values | Integers can be positive or negative

## Slide 3
Unsigned Integer
Weight | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
Coefficient | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
8-bit Example

## Slide 4
Unsigned Integer
Weight | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
Coefficient | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
= 27 + 24 + 23 + 20
= 128 + 16 + 8 + 1
= 153
8-bit Example

## Slide 5
Unsigned Integer
Minimum | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
8-bit Example

## Slide 6
Unsigned Integer
Minimum | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
8-bit Example
= 0

## Slide 7
Unsigned Integer
Maximum | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
8-bit Example

## Slide 8
Unsigned Integer
Maximum | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
8-bit Example
= 27 + 26 + 25 + 24 + 23 + 22 + 21 + 20
= 128 + 64 + 32 + 16 + 8 + 4 + 2 + 1
= 255

## Slide 9
Unsigned Integer
Maximum | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
 |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
8-bit Example
+
1

## Slide 10
Unsigned Integer
Maximum | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
 |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
8-bit Example
+
1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 11
Unsigned Integer
Maximum | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
 |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
8-bit Example
+
1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
= 28 = 256

## Slide 12
Unsigned Integer
Maximum | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
8-bit Example
= 256 – 1 = 255

## Slide 13
Unsigned Integer
Range of 8-bit unsigned integer
0 ~ 28 - 1

## Slide 14
Unsigned Integer
Range of 8-bit unsigned integer
0 ~ 28 - 1
Range of n-bit unsigned integer

## Slide 15
Unsigned Integer
Range of 8-bit unsigned integer
0 ~ 28 - 1
Range of n-bit unsigned integer
0 ~ 2n - 1

## Slide 16
Signed Integer
Sign & Magnitude
1’s Complement
2’s Complement

## Slide 17
Signed Integer-Sign & Magnitude
How to express 4-bit S&M -5?
Example 1

## Slide 18
Signed Integer-Sign & Magnitude
How to express 4-bit S&M -5?
- | 5
Sign
Magnitude
Example 1

## Slide 19
Signed Integer-Sign & Magnitude
How to express 4-bit S&M -5?
- | 5
Sign
Magnitude
Sign
Magnitude
Example 1

## Slide 20
Signed Integer-Sign & Magnitude
How to express 4-bit S&M -5?
 | 1 | 0 | 1
Sign
Magnitude
- | 5
Sign
Magnitude
Example 1

## Slide 21
Signed Integer-Sign & Magnitude
How to express 4-bit S&M -5?
1 | 1 | 0 | 1
Sign
Magnitude
- | 5
Sign
Magnitude
Example 1

## Slide 22
Signed Integer-Sign & Magnitude
How to express 4-bit S&M -5?
1 | 1 | 0 | 1
Example 1

## Slide 23
Signed Integer-Sign & Magnitude
How to express 4-bit S&M +3?
Example 2

## Slide 24
Signed Integer-Sign & Magnitude
How to express 4-bit S&M +3?
+ | 3
Sign
Magnitude
Example 2

## Slide 25
Signed Integer-Sign & Magnitude
How to express 4-bit S&M +3?
+ | 3
Sign
Magnitude
Sign
Magnitude
Example 2

## Slide 26
Signed Integer-Sign & Magnitude
How to express 4-bit S&M +3?
 | 0 | 1 | 1
Sign
Magnitude
+ | 3
Sign
Magnitude
Example 2

## Slide 27
Signed Integer-Sign & Magnitude
How to express 4-bit S&M +3?
0 | 0 | 1 | 1
Sign
Magnitude
+ | 3
Sign
Magnitude
Example 2

## Slide 28
Signed Integer-Sign & Magnitude
How to express 4-bit S&M +3?
0 | 0 | 1 | 1
Example 2

## Slide 29
Signed Integer-Sign & Magnitude
4-bit Sign & Magnitude
0 000 | = | + 0
0 001 | = | + 1
0 010 | = | + 2
0 011 | = | + 3
0 100 | = | + 4
0 101 | = | + 5
0 110 | = | + 6
0 111 | = | + 7
1 000 | = | - 0
1 001 | = | - 1
1 010 | = | - 2
1 011 | = | - 3
1 100 | = | - 4
1 101 | = | - 5
1 110 | = | - 6
1 111 | = | - 7

## Slide 30
Signed Integer-Sign & Magnitude
ADVANTAGE of signed magnitude:
You can determine whether a number is negative or non negative simply by testing the most significant bit.

## Slide 31
Signed Integer-Sign & Magnitude
DISADVANTAGES of signed magnitude:
There are two notations for 0 (0000 and 1111), which is very inconvenient when the computer wants to test for a 0 result.
Addition doesn't work the way we want it to.

## Slide 32
Signed Integer-Sign & Magnitude
0 | 0 | 1 | 1
1 | 0 | 1 | 0
+3
+
- 2
4-bit Sign & Magnitude

## Slide 33
Signed Integer-Sign & Magnitude
0 | 0 | 1 | 1
1 | 0 | 1 | 0
+3
+
1 | 1 | 0 | 1
- 2
4-bit Sign & Magnitude

## Slide 34
Signed Integer-Sign & Magnitude
0 | 0 | 1 | 1
1 | 0 | 1 | 0
+3
- 2
+
1 | 1 | 0 | 1
- 5
4-bit Sign & Magnitude

## Slide 35
Signed Integer-Sign & Magnitude
0 | 0 | 1 | 1
1 | 0 | 1 | 0
+3
- 2
+
1 | 1 | 0 | 1
- 5
4-bit Sign & Magnitude

## Slide 36
Signed Integer-Sign & 1’s complement
How to express 4-bit 1’s complement -5?
0 | 1 | 0 | 1
Unsigned 5
Example 1

## Slide 37
Signed Integer-Sign & 1’s complement
How to express 4-bit 1’s complement -5?
0 | 1 | 0 | 1
Unsigned 5
0 | 1 | 0 | 1
1’s complement + 5
Example 1

## Slide 38
Signed Integer-Sign & 1’s complement
How to express 4-bit 1’s complement -5?
0 | 1 | 0 | 1
Unsigned 5
0 | 1 | 0 | 1
1’s complement + 5
1’s complement - 5
Example 1

## Slide 39
Signed Integer-Sign & 1’s complement
How to express 4-bit 1’s complement -5?
0 | 1 | 0 | 1
Unsigned 5
0 | 1 | 0 | 1
1’s complement + 5
1 | 0 | 1 | 0
1’s complement - 5
Example 1

## Slide 40
Signed Integer-Sign & 1’s complement
How to express 4-bit 1’s complement -7?
0 | 1 | 1 | 1
Unsigned 7
Example 2

## Slide 41
Signed Integer-Sign & 1’s complement
How to express 4-bit 1’s complement -7?
0 | 1 | 1 | 1
Unsigned 7
0 | 1 | 1 | 1
1’s complement + 7
Example 2

## Slide 42
Signed Integer-Sign & 1’s complement
How to express 4-bit 1’s complement -7?
0 | 1 | 1 | 1
Unsigned 7
0 | 1 | 1 | 1
1’s complement + 7
1’s complement - 7
Example 2

## Slide 43
Signed Integer-Sign & 1’s complement
How to express 4-bit 1’s complement -7?
0 | 1 | 1 | 1
Unsigned 7
0 | 1 | 1 | 1
1’s complement + 7
1 | 0 | 0 | 0
1’s complement - 7
Example 2

## Slide 44
4-bit 1’s complement
0000 | = | + 0
0001 | = | + 1
0010 | = | + 2
0011 | = | + 3
0100 | = | + 4
0101 | = | + 5
0110 | = | + 6
0111 | = | + 7
1000 | = | - 7
1001 | = | - 6
1010 | = | - 5
1011 | = | - 4
1100 | = | - 3
1101 | = | - 2
1110 | = | - 1
1111 | = | - 0
Signed Integer-Sign & 1’s complement

## Slide 45
Signed Integer-Sign & 1’s complement
Advantages
It is easy to convert a positive number to its corresponding negative number, vice versa.

## Slide 46
Signed Integer-Sign & 1’s complement
Disadvantage
There are two notations for 0 (0000 and 1000), which is very inconvenient when the computer wants to test for a 0 result.
To get the correct answer after addition, the result of addition and final carry has to be added up.

## Slide 47
Signed Integer-Sign & 1’s complement
1 | 1 | 0 | 0
1 | 1 | 0 | 1
- 3
+
- 2
4-bit 1’s complement

## Slide 48
Signed Integer-Sign & 1’s complement
1 | 1 | 0 | 0
1 | 1 | 0 | 1
- 3
+
- 2
4-bit 1’s complement
1 | 0 | 0 | 1
1

## Slide 49
Signed Integer-Sign & 1’s complement
1 | 1 | 0 | 0
1 | 1 | 0 | 1
- 3
+
- 2
4-bit 1’s complement
1 | 0 | 0 | 1
1

## Slide 50
Signed Integer-Sign & 1’s complement
1 | 1 | 0 | 0
1 | 1 | 0 | 1
- 3
+
- 2
4-bit 1’s complement
1 | 0 | 0 | 1
- 6
1

## Slide 51
Signed Integer-Sign & 1’s complement
1 | 1 | 0 | 0
1 | 1 | 0 | 1
- 3
+
- 2
4-bit 1’s complement
1 | 0 | 0 | 1
- 6
1

## Slide 52
Signed Integer-Sign & 1’s complement
1 | 1 | 0 | 0
1 | 1 | 0 | 1
- 3
+
- 2
4-bit 1’s complement
1 | 0 | 0 | 1
1
+

## Slide 53
Signed Integer-Sign & 1’s complement
1 | 1 | 0 | 0
1 | 1 | 0 | 1
- 3
+
- 2
4-bit 1’s complement
1 | 0 | 0 | 1
1
+

## Slide 54
Signed Integer-Sign & 1’s complement
1 | 1 | 0 | 0
1 | 1 | 0 | 1
- 3
+
- 2
4-bit 1’s complement
1 | 0 | 0 | 1
1
+
1 | 0 | 1 | 0

## Slide 55
Signed Integer-Sign & 1’s complement
1 | 1 | 0 | 0
1 | 1 | 0 | 1
- 3
+
- 2
4-bit 1’s complement
1 | 0 | 0 | 1
1
+
1 | 0 | 1 | 0
- 5

## Slide 56
Signed Integer-Sign & 1’s complement
1 | 1 | 0 | 0
1 | 1 | 0 | 1
- 3
+
- 2
4-bit 1’s complement
1 | 0 | 0 | 1
1
+
1 | 0 | 1 | 0
- 5


## Slide 57
Signed Integer-Sign & 1’s complement
1 | 1 | 0 | 0
1 | 1 | 0 | 1
- 3
+
- 2
4-bit 1’s complement
1 | 0 | 0 | 1
1
+
1 | 0 | 1 | 0
- 5
End round carry correction


## Slide 58
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -5?
Example 1

## Slide 59
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -5?
0 | 1 | 0 | 1
Unsigned 5
Example 1

## Slide 60
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -5?
0 | 1 | 0 | 1
Unsigned 5
0 | 1 | 0 | 1
2’s complement + 5
Example 1

## Slide 61
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -5?
0 | 1 | 0 | 1
Unsigned 5
0 | 1 | 0 | 1
2’s complement + 5
1 | 0 | 1 | 0
Example 1

## Slide 62
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -5?
0 | 1 | 0 | 1
Unsigned 5
0 | 1 | 0 | 1
2’s complement + 5
1 | 0 | 1 | 0
1
+
Example 1

## Slide 63
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -5?
0 | 1 | 0 | 1
Unsigned 5
0 | 1 | 0 | 1
2’s complement + 5
1 | 0 | 1 | 0
1
+
1 | 0 | 1 | 1
Example 1

## Slide 64
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -5?
0 | 1 | 0 | 1
Unsigned 5
0 | 1 | 0 | 1
2’s complement + 5
1 | 0 | 1 | 0
2’s complement - 5
1
+
1 | 0 | 1 | 1
Example 1

## Slide 65
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -7?
Example 2

## Slide 66
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -7?
0 | 1 | 1 | 1
Unsigned 7
Example 2

## Slide 67
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -7?
0 | 1 | 1 | 1
Unsigned 7
0 | 1 | 1 | 1
2’s complement + 7
Example 2

## Slide 68
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -7?
0 | 1 | 1 | 1
Unsigned 7
0 | 1 | 1 | 1
2’s complement + 7
1 | 0 | 0 | 0
Example 2

## Slide 69
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -7?
0 | 1 | 1 | 1
Unsigned 7
0 | 1 | 1 | 1
2’s complement + 7
1 | 0 | 0 | 0
1
+
Example 2

## Slide 70
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -7?
0 | 1 | 1 | 1
Unsigned 7
0 | 1 | 1 | 1
2’s complement + 7
1 | 0 | 0 | 0
1
+
1 | 0 | 0 | 1
Example 2

## Slide 71
Signed Integer-Sign & 2’s complement
How to express 4-bit 2’s complement -7?
0 | 1 | 1 | 1
Unsigned 7
0 | 1 | 1 | 1
2’s complement + 7
1 | 0 | 0 | 0
2’s complement - 7
1
+
1 | 0 | 0 | 1
Example 2

## Slide 72
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
0 | 1 | 1 | 0
2’s complement + 6
Example 1

## Slide 73
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
0 | 1 | 1 | 0
Example 1

## Slide 74
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
0 | 1 | 1 | 0
Example 1

## Slide 75
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
0 | 1 | 1 | 0
Example 1

## Slide 76
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
1 | 0 | 1 | 0
Example 1

## Slide 77
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
1 | 0 | 1 | 0
Example 1

## Slide 78
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
1 | 0 | 1 | 0
2’s complement - 6
Example 1

## Slide 79
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
2’s complement -100
Example 2

## Slide 80
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
Example 2

## Slide 81
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
Example 2

## Slide 82
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
Example 2

## Slide 83
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
Example 2

## Slide 84
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
Example 2

## Slide 85
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
2’s complement +100
Example 2

## Slide 86
Signed Integer-Sign & 2’s complement
Shortcut for taking 2’s complement.
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
2’s complement +100
Example 2
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
2’s complement -100

## Slide 87
Signed Integer-Sign & 2’s complement
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
2’s complement -100
Weights for a 2’s complement number.

## Slide 88
Signed Integer-Sign & 2’s complement
-27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
2’s complement -100
Weights for a 2’s complement number.
weight
Negative

## Slide 89
Signed Integer-Sign & 2’s complement
-27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
2’s complement -100
Weights for a 2’s complement number.
weight
= -27 + 24 + 23 + 22
= -128 + 16 + 8 + 4
= -100
Negative

## Slide 90
Signed Integer-Sign & 2’s complement
Given the bit pattern 10010011, what does it represent assuming
It’s a two’s complement integer?
It’s an unsigned integer?
Write down your answer in decimal format.

## Slide 91
Signed Integer-Sign & 2’s complement
Given the bit pattern 10010011, what does it represent assuming
It’s a two’s complement integer?.
-27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 0 | 0 | 1 | 0 | 0 | 1 | 1

## Slide 92
Signed Integer-Sign & 2’s complement
Given the bit pattern 10010011, what does it represent assuming
It’s a two’s complement integer?.
-27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
= -27 + 24 + 21 + 20
= -128 + 16 + 2 + 1
= -109

## Slide 93
Signed Integer-Sign & 2’s complement
Given the bit pattern 10010011, what does it represent assuming
It’s an unsigned integer?
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 0 | 0 | 1 | 0 | 0 | 1 | 1

## Slide 94
Signed Integer-Sign & 2’s complement
Given the bit pattern 10010011, what does it represent assuming
It’s an unsigned integer?
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
= 27 + 24 + 21 + 20
= 128 + 16 + 2 + 1
= 147

## Slide 95
Signed Integer-Sign & 2’s complement
4-bit 2’s complement
0000 | = | + 0
0001 | = | + 1
0010 | = | + 2
0011 | = | + 3
0100 | = | + 4
0101 | = | + 5
0110 | = | + 6
0111 | = | + 7
1000 | = | - 8
1001 | = | - 7
1010 | = | - 6
1011 | = | - 5
1100 | = | - 4
1101 | = | - 3
1110 | = | - 2
1111 | = | - 1

## Slide 96
Signed Integer-Sign & 2’s complement
Advantage:
Two's complement has only one 0.
Compared to other systems for representing signed numbers, two's complement has the advantage that the fundamental arithmetic operations are identical to those for unsigned binary numbers

## Slide 97
Signed Integer-Sign & 2’s complement
0000
2’s complement +0

## Slide 98
Signed Integer-Sign & 2’s complement
0000
1111
2’s complement +0

## Slide 99
Signed Integer-Sign & 2’s complement
0000
1111
1111
+
1 0000
2’s complement +0

## Slide 100
Signed Integer-Sign & 2’s complement
0000
1111
1111
+
1 0000
2’s complement +0

## Slide 101
Signed Integer-Sign & 2’s complement
0000
1111
1111
+
1 0000
2’s complement +0
2’s complement -0

## Slide 102
Signed Integer-Sign & 2’s complement
0000
1111
1111
+
1 0000
2’s complement +0
2’s complement -0
Two's complement has only one 0

## Slide 103
Signed Integer-Sign & 2’s complement
1 | 1 | 0 | 1
1 | 1 | 1 | 0
- 3
+
- 2
4-bit 2’s complement

## Slide 104
Signed Integer-Sign & 2’s complement
1 | 1 | 0 | 1
1 | 1 | 1 | 0
- 3
+
- 2
4-bit 2’s complement
1 | 0 | 1 | 1
1

## Slide 105
Signed Integer-Sign & 2’s complement
1 | 1 | 0 | 1
1 | 1 | 1 | 0
- 3
+
- 2
4-bit 2’s complement
1 | 0 | 1 | 1
1
- 5

## Slide 106
Signed Integer-Sign & 2’s complement
1 | 1 | 0 | 1
1 | 1 | 1 | 0
- 3
+
- 2
4-bit 2’s complement
1 | 0 | 1 | 1
1
- 5


## Slide 107
Signed Integer-Sign & 2’s complement
1 | 1 | 0 | 1
1 | 1 | 1 | 0
- 3
+
- 2
4-bit 2’s complement
1 | 0 | 1 | 1
1
- 5

The fundamental arithmetic operations are identical to those for unsigned binary numbers

## Slide 108
Binary | Sign & Magnitude | 1’s complement | 2’s complement
0000 | + 0 | + 0 | + 0
0001 | + 1 | + 1 | + 1
0010 | + 2 | + 2 | + 2
0011 | + 3 | + 3 | + 3
0100 | + 4 | + 4 | + 4
0101 | + 5 | + 5 | + 5
0110 | + 6 | + 6 | + 6
0111 | + 7 | + 7 | + 7
1000 | - 0 | - 7 | - 8
1001 | - 1 | - 6 | - 7
1010 | - 2 | - 5 | - 6
1011 | - 3 | - 4 | - 5
1100 | - 4 | - 3 | - 4
1101 | - 5 | - 2 | - 3
1110 | - 6 | - 1 | - 2
1111 | - 7 | - 0 | - 1

## Slide 109
Modern computer use 2’s complement to represent signed integer

## Slide 110
Exercise-1
What unsigned binary number is represented by the string of bits 11001?

## Slide 111
Exercise-1
What unsigned binary number is represented by the string of bits 11001?
= 16 + 8 + 1 = 2510
16 | 8 | 4 | 2 | 1
1 | 1 | 0 | 0 | 1
weight

## Slide 112
Exercise-2
What decimal number does the signed-magnitude binary number
N = 10011 represent?

## Slide 113
Exercise-2
What decimal number does the signed-magnitude binary number
N = 10011 represent?
Sign | Magnitude |  |  | 
 | 8 | 4 | 2 | 1
1 | 0 | 0 | 1 | 1
weight
= ­­- (2 + 1) = - 3

## Slide 114
Exercise-3
Represent −10510 three ways with 8 bits:
signed-magnitude
signed 1’s complement, and
signed 2’s complement.

## Slide 115
Exercise-3
Convert 10510 to 8-bit unsigned binary number
Integer | Remainder
105 | 
52 | 1
26 | 0
13 | 0
6 | 1
3 | 0
1 | 1
0 | 1
10510 = 011010012

## Slide 116
Exercise-3
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
Unsigned 105

## Slide 117
Exercise-3
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
Unsigned 105
(a) Sign & Magnitude - 105

## Slide 118
Exercise-3
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
 | 1 | 1 | 0 | 1 | 0 | 0 | 1
Magnitude
Unsigned 105
(a) Sign & Magnitude - 105

## Slide 119
Exercise-3
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
Unsigned 105
1 | 1 | 1 | 0 | 1 | 0 | 0 | 1
Sign
(a) Sign & Magnitude - 105

## Slide 120
Exercise-3
1 | 1 | 1 | 0 | 1 | 0 | 0 | 1
(a) Sign & Magnitude - 105

## Slide 121
Exercise-3
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
Unsigned 105
(b) 1’s complement - 105

## Slide 122
Exercise-3
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
Unsigned 105
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0
(b) 1’s complement - 105

## Slide 123
Exercise-3
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0
(b) 1’s complement - 105

## Slide 124
Exercise-3
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
Unsigned 105
(c) 2’s complement - 105

## Slide 125
Exercise-3
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
Unsigned 105
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0
(c) 2’s complement - 105

## Slide 126
Exercise-3
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
Unsigned 105
1 | 0 | 0 | 1 | 0 | 1 | 1 | 1
(c) 2’s complement - 105

## Slide 127
Exercise-3
1 | 0 | 0 | 1 | 0 | 1 | 1 | 1
(c) 2’s complement - 105

## Slide 128
Exercise-3
1 | 1 | 1 | 0 | 1 | 0 | 0 | 1
Sign & Magnitude - 105
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0
1’s complement - 105
1 | 0 | 0 | 1 | 0 | 1 | 1 | 1
2’s complement - 105

## Slide 129
Lecture 2
Binary Numbers
Decimal fraction to non-decimal fraction

## Slide 130
Decimal Fraction to non-Decimal fraction
0 | 0 | 0 | 0 | 1 | 0 |  | 
Corresponding binary number
Decimal number
2 |  | 

## Slide 131
Decimal Fraction to non-Decimal fraction
0 | 0 | 0 | 0 | 1 | 0 |  | 2
Corresponding binary number
Decimal number
2 |  | 2

## Slide 132
Decimal Fraction to non-Decimal fraction
0 | 0 | 0 | 0 | 1 | 0 |  | 2
Corresponding binary number
Decimal number
2 |  | 2
=
=
0 | 0 | 0 | 1 | 0 | 0 |  | 
4 |  | 

## Slide 133
Decimal Fraction to non-Decimal fraction
0 | 0 | 0 | 0 | 1 | 0 |  | 2
Corresponding binary number
Decimal number
2 |  | 2
=
=
0 | 0 | 0 | 1 | 0 | 0 |  | 2
4 |  | 2
=
=

## Slide 134
Decimal Fraction to non-Decimal fraction
0 | 0 | 0 | 0 | 1 | 0 |  | 2
Corresponding binary number
Decimal number
2 |  | 2
=
=
0 | 0 | 0 | 1 | 0 | 0 |  | 2
4 |  | 2
=
=
0 | 0 | 1 | 0 | 0 | 0 |  | 
8 |  | 

## Slide 135
Decimal Fraction to non-Decimal fraction
0 | 0 | 0 | 0 | 1 | 0 |  | 2
Corresponding binary number
Decimal number
2 |  | 2
=
=
0 | 0 | 0 | 1 | 0 | 0 |  | 2
4 |  | 2
=
=
0 | 0 | 1 | 0 | 0 | 0 |  | 2
8 |  | 2
=
=

## Slide 136
Decimal Fraction to non-Decimal fraction
0 | 0 | 0 | 0 | 1 | 0 |  | 2
Corresponding binary number
Decimal number
2 |  | 2
=
=
0 | 0 | 0 | 1 | 0 | 0 |  | 2
4 |  | 2
=
=
0 | 0 | 1 | 0 | 0 | 0 |  | 2
8 |  | 2
=
=
0 | 1 | 0 | 0 | 0 | 0 |  | 
16 |  | 

## Slide 137
Decimal Fraction to non-Decimal fraction
0 | 0 | 0 | 0 | 1 | 0 |  | 2
=
0 | 0 | 0 | 1 | 0 | 0 |  | 2
=
0 | 0 | 1 | 0 | 0 | 0 |  | 2
=
0 | 1 | 0 | 0 | 0 | 0 |  | 
Shift a binary number left is equal to multiply the number by power of 2

## Slide 138
Decimal Fraction to non-Decimal fraction
Decimal
Binary

## Slide 139
Decimal Fraction to non-Decimal fraction
Decimal
0.6875
. | a-1 | a-2 | a-3 | a-4 | ….
=
Binary

## Slide 140
Decimal Fraction to non-Decimal fraction
Decimal
0.6875
. | a-1 | a-2 | a-3 | a-4 | ….
=
a-1 | a-2 | a-3 | a-4 | ….
Round 1
Binary

## Slide 141
Decimal Fraction to non-Decimal fraction
Decimal
Binary
0.6875
. | a-1 | a-2 | a-3 | a-4 | ….
=
 | 2
 | 2
a-1 | a-2 | a-3 | a-4 | ….
Round 1

## Slide 142
Decimal Fraction to non-Decimal fraction
Decimal
0.6875
. | a-1 | a-2 | a-3 | a-4 | ….
=
 | 2
 | 2
a-1 | a-2 | a-3 | a-4 | ….
1.375
. | a-2 | a-3 | a-4 | a-5 | ….
a-1
=
Round 1
Binary

## Slide 143
Decimal Fraction to non-Decimal fraction
Decimal
0.6875
. | a-1 | a-2 | a-3 | a-4 | ….
=
 | 2
 | 2
a-1 | a-2 | a-3 | a-4 | ….
1 |  |  |  | 
1.375
. | a-2 | a-3 | a-4 | a-5 | ….
a-1
=
1.375
. | a-2 | a-3 | a-4 | a-5 | ….
a-1
=
Round 1
Binary

## Slide 144
Decimal Fraction to non-Decimal fraction
Decimal
0.6875
. | a-1 | a-2 | a-3 | a-4 | ….
=
 | 2
 | 2
a-1 | a-2 | a-3 | a-4 | ….
1.375
. | a-2 | a-3 | a-4 | a-5 | ….
a-1
=
1.375
. | a-2 | a-3 | a-4 | a-5 | ….
a-1
=
1.375
. | a-2 | a-3 | a-4 | a-5 | ….
a-1
=
Round 1
Binary

## Slide 145
Decimal Fraction to non-Decimal fraction
Decimal
0.6875
. | a-1 | a-2 | a-3 | a-4 | ….
=
 | 2
 | 2
1.375
. | a-2 | a-3 | a-4 | a-5 | ….
a-1
=
1.375
. | a-2 | a-3 | a-4 | a-5 | ….
a-1
=
1.375
. | a-2 | a-3 | a-4 | a-5 | ….
a-1
=
a-1 | a-2 | a-3 | a-4 | ….
1 |  |  |  | 
Round 1
Binary

## Slide 146
Decimal Fraction to non-Decimal fraction
Decimal
0.375
. | a-2 | a-3 | a-4 | a-5 | ….
=
Round 2
a-1 | a-2 | a-3 | a-4 | ….
1 |  |  |  | 
Binary

## Slide 147
Decimal Fraction to non-Decimal fraction
Decimal
0.375
. | a-2 | a-3 | a-4 | a-5 | ….
=
 | 2
 | 2
Round 2
a-1 | a-2 | a-3 | a-4 | ….
1 |  |  |  | 
Binary

## Slide 148
Decimal Fraction to non-Decimal fraction
Decimal
0.375
. | a-2 | a-3 | a-4 | a-5 | ….
=
 | 2
 | 2
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
a-2
=
Round 2
a-1 | a-2 | a-3 | a-4 | ….
1 |  |  |  | 
Binary

## Slide 149
Decimal Fraction to non-Decimal fraction
Decimal
0.375
. | a-2 | a-3 | a-4 | a-5 | ….
=
 | 2
 | 2
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
a-2
=
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
a-2
=
Round 2
a-1 | a-2 | a-3 | a-4 | ….
1 |  |  |  | 
Binary

## Slide 150
Decimal Fraction to non-Decimal fraction
Decimal
0.375
. | a-2 | a-3 | a-4 | a-5 | ….
=
 | 2
 | 2
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
a-2
=
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
a-2
=
Round 2
a-1 | a-2 | a-3 | a-4 | ….
1 |  |  |  | 
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
a-2
=
Binary

## Slide 151
Decimal Fraction to non-Decimal fraction
Decimal
0.375
. | a-2 | a-3 | a-4 | a-5 | ….
=
 | 2
 | 2
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
a-2
=
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
a-2
=
Round 2
a-1 | a-2 | a-3 | a-4 | ….
1 | 0 |  |  | 
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
a-2
=
Binary

## Slide 152
Decimal Fraction to non-Decimal fraction
Decimal
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
=
Round 3
a-1 | a-2 | a-3 | a-4 | ….
1 | 0 |  |  | 
Binary

## Slide 153
Decimal Fraction to non-Decimal fraction
Decimal
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
=
 | 2
 | 2
Round 3
a-1 | a-2 | a-3 | a-4 | ….
1 | 0 |  |  | 
1.5
. | a-4 | a-5 | a-6 | a-7 | ….
a-3
=
Binary

## Slide 154
Decimal Fraction to non-Decimal fraction
Decimal
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
=
 | 2
 | 2
Round 3
a-1 | a-2 | a-3 | a-4 | ….
1 | 0 |  |  | 
1.5
. | a-4 | a-5 | a-6 | a-7 | ….
a-3
=
1.5
. | a-4 | a-5 | a-6 | a-7 | ….
a-3
=
Binary

## Slide 155
Decimal Fraction to non-Decimal fraction
Decimal
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
=
 | 2
 | 2
Round 3
a-1 | a-2 | a-3 | a-4 | ….
1 | 0 |  |  | 
1.5
. | a-4 | a-5 | a-6 | a-7 | ….
a-3
=
1.5
. | a-4 | a-5 | a-6 | a-7 | ….
a-3
=
1.5
. | a-4 | a-5 | a-6 | a-7 | ….
a-3
=
Binary

## Slide 156
Decimal Fraction to non-Decimal fraction
Decimal
0.75
. | a-3 | a-4 | a-5 | a-6 | ….
=
 | 2
 | 2
Round 3
a-1 | a-2 | a-3 | a-4 | ….
1 | 0 | 1 |  | 
1.5
. | a-4 | a-5 | a-6 | a-7 | ….
a-3
=
1.5
. | a-4 | a-5 | a-6 | a-7 | ….
a-3
=
1.5
. | a-4 | a-5 | a-6 | a-7 | ….
a-3
=
Binary

## Slide 157
Decimal Fraction to non-Decimal fraction
Decimal
0.5
. | a-4 | a-5 | a-6 | a-7 | ….
=
Round 4
a-1 | a-2 | a-3 | a-4 | ….
1 | 0 | 1 |  | 
Binary

## Slide 158
Decimal Fraction to non-Decimal fraction
Decimal
0.5
. | a-4 | a-5 | a-6 | a-7 | ….
=
 | 2
 | 2
Round 4
a-1 | a-2 | a-3 | a-4 | ….
1 | 0 | 1 |  | 
Binary

## Slide 159
Decimal Fraction to non-Decimal fraction
Decimal
0.5
. | a-4 | a-5 | a-6 | a-7 | ….
=
 | 2
 | 2
Round 4
a-1 | a-2 | a-3 | a-4 | ….
1 | 0 | 1 |  | 
1.0
. | a-5 | a-6 | a-7 | a-8 | ….
a-4
=
Binary

## Slide 160
Decimal Fraction to non-Decimal fraction
Decimal
0.5
. | a-4 | a-5 | a-6 | a-7 | ….
=
 | 2
 | 2
Round 4
a-1 | a-2 | a-3 | a-4 | ….
1 | 0 | 1 |  | 
1.0
. | a-5 | a-6 | a-7 | a-8 | ….
a-4
=
1.0
. | a-4 | a-5 | a-6 | a-7 | ….
a-4
=
Binary

## Slide 161
Decimal Fraction to non-Decimal fraction
Decimal
0.5
. | a-4 | a-5 | a-6 | a-7 | ….
=
 | 2
 | 2
Round 4
a-1 | a-2 | a-3 | a-4 | ….
1 | 0 | 1 |  | 
1.0
. | a-5 | a-6 | a-7 | a-8 | ….
a-4
=
1.0
. | a-4 | a-5 | a-6 | a-7 | ….
a-4
=
1.0
. | a-5 | a-6 | a-7 | a-8 | ….
a-4
=
Binary

## Slide 162
Decimal Fraction to non-Decimal fraction
Decimal
0.5
. | a-4 | a-5 | a-6 | a-7 | ….
=
 | 2
 | 2
Round 4
a-1 | a-2 | a-3 | a-4 | ….
1 | 0 | 1 | 1 | 
1.0
. | a-5 | a-6 | a-7 | a-8 | ….
a-4
=
1.0
. | a-4 | a-5 | a-6 | a-7 | ….
a-4
=
1.0
. | a-5 | a-6 | a-7 | a-8 | ….
a-4
=
Binary

## Slide 163
Decimal Fraction to non-Decimal fraction
Decimal
0.5
. | a-4 | a-5 | a-6 | a-7 | ….
=
 | 2
 | 2
Round 4
a-1 | a-2 | a-3 | a-4 | 
1 | 0 | 1 | 1 | 
1.0
. | a-5 | a-6 | a-7 | a-8 | ….
a-4
=
1.0
. | a-4 | a-5 | a-6 | a-7 | ….
a-4
=
1.0
. | a-5 | a-6 | a-7 | a-8 | ….
a-4
=
Binary

## Slide 164
Decimal Fraction to non-Decimal fraction
0.687510 = 0.10112
a-1 | a-2 | a-3 | a-4
1 | 0 | 1 | 1

## Slide 165
Decimal Fraction to non-Decimal fraction
0.6875  2 |  |  |  |  | 

## Slide 166
Decimal Fraction to non-Decimal fraction
0.6875  2 |  |  |  |  | 

## Slide 167
Decimal Fraction to non-Decimal fraction
 |  | Integer |  | Fraction | Coefficient
0.6875  2 | = | 1 | + | 0.3750 | a-1 = 1

## Slide 168
Decimal Fraction to non-Decimal fraction
 |  | Integer |  | Fraction | Coefficient
0.6875  2 | = | 1 | + | 0.3750 | a-1 = 1
0.3750  2 | = | 0 | + | 0.7500 | a-2 = 0

## Slide 169
Decimal Fraction to non-Decimal fraction
 |  | Integer |  | Fraction | Coefficient
0.6875  2 | = | 1 | + | 0.3750 | a-1 = 1
0.3750  2 | = | 0 | + | 0.7500 | a-2 = 0
0.7500  2 | = | 1 | + | 0.5000 | a-3 = 1

## Slide 170
Decimal Fraction to non-Decimal fraction
 |  | Integer |  | Fraction | Coefficient
0.6875  2 | = | 1 | + | 0.3750 | a-1 = 1
0.3750  2 | = | 0 | + | 0.7500 | a-2 = 0
0.7500  2 | = | 1 | + | 0.5000 | a-3 = 1
0.5000  2 | = | 1 | + | 0.0000 | a-4 = 1

## Slide 171
Decimal Fraction to non-Decimal fraction
 |  | Integer |  | Fraction | Coefficient
0.6875  2 | = | 1 | + | 0.3750 | a-1 = 1
0.3750  2 | = | 0 | + | 0.7500 | a-2 = 0
0.7500  2 | = | 1 | + | 0.5000 | a-3 = 1
0.5000  2 | = | 1 | + | 0.0000 | a-4 = 1
0.6875

## Slide 172
Decimal Fraction to non-Decimal fraction
 |  | Integer |  | Fraction | Coefficient
0.6875  2 | = | 1 | + | 0.3750 | a-1 = 1
0.3750  2 | = | 0 | + | 0.7500 | a-2 = 0
0.7500  2 | = | 1 | + | 0.5000 | a-3 = 1
0.5000  2 | = | 1 | + | 0.0000 | a-4 = 1
= .10112
0.6875

## Slide 173
Decimal Fraction to non-Decimal fraction
To convert a decimal fraction to a number expressed in base r, a similar procedure is used. However, multiplication is by r instead of 2, and the coefficients found from the integers may range in value from 0 to r  1 instead of 0 and 1.

## Slide 174
Decimal Fraction to non-Decimal fraction
Convert 0.51310 to octal.

## Slide 175
Decimal Fraction to non-Decimal fraction
0.513  8 | = | 4.104
0.104  8 | = | 0.832
0.832  8 | = | 6.656
0.656  8 | = | 5.248
0.248  8 | = | 1.984
0.984  8 | = | 7.872
Convert 0.51310 to octal.

## Slide 176
Decimal Fraction to non-Decimal fraction
0.513  8 | = | 4.104
0.104  8 | = | 0.832
0.832  8 | = | 6.656
0.656  8 | = | 5.248
0.248  8 | = | 1.984
0.984  8 | = | 7.872
0.51310 = 0.406517…. 8
Convert 0.51310 to octal.

## Slide 177
Decimal Fraction to non-Decimal fraction
0.513  8 | = | 4.104
0.104  8 | = | 0.832
0.832  8 | = | 6.656
0.656  8 | = | 5.248
0.248  8 | = | 1.984
0.984  8 | = | 7.872
0.51310 = 0.406517…. 8
infinite decimal
Convert 0.51310 to octal.

## Slide 178
Decimal Fraction to non-Decimal fraction
Convert 57.812510 to binary.

## Slide 179
Decimal Fraction to non-Decimal fraction
Convert 57.812510 to binary.

## Slide 180
Decimal Fraction to non-Decimal fraction
Convert 57.812510 to binary.
Integer | Remainder
57 | 
28 | 1
14 | 0
7 | 0
3 | 1
1 | 1
0 | 1

## Slide 181
Decimal Fraction to non-Decimal fraction
Convert 57.812510 to binary.
Integer | Remainder
57 | 
28 | 1
14 | 0
7 | 0
3 | 1
1 | 1
0 | 1
111001.

## Slide 182
Decimal Fraction to non-Decimal fraction
Convert 57.812510 to binary.
Integer | Remainder
57 | 
28 | 1
14 | 0
7 | 0
3 | 1
1 | 1
0 | 1
111001.
0.8125  2 | = | 1.6250
0.6250  2 | = | 1.2500
0.2500  2 | = | 0.5000
0.5000  2 | = | 1.0000

## Slide 183
Decimal Fraction to non-Decimal fraction
Convert 57.812510 to binary.
Integer | Remainder
57 | 
28 | 1
14 | 0
7 | 0
3 | 1
1 | 1
0 | 1
111001.
0.8125  2 | = | 1.6250
0.6250  2 | = | 1.2500
0.2500  2 | = | 0.5000
0.5000  2 | = | 1.0000
.1101

## Slide 184
Decimal Fraction to non-Decimal fraction
Convert 57.812510 to binary.
Integer | Remainder
57 | 
28 | 1
14 | 0
7 | 0
3 | 1
1 | 1
0 | 1
111001.
0.8125  2 | = | 1.6250
0.6250  2 | = | 1.2500
0.2500  2 | = | 0.5000
0.5000  2 | = | 1.0000
.1101
111001.1101

## Slide 185
Decimal Fraction to non-Decimal fraction
57.812510 = 111001.11012

## Slide 186: thanks