## Slide 1
Boolean Algebra |  | 
A set of element | A set of operators | A set of postulates
S = {1, 2, 3, ….} | B = {+ , - , ….} | Closure
 |  | Commutative law
 |  | Distributive law
 |  | Identity element
 |  | Complement
 |  | ¦S¦ ≥ 2
Provide basic assumptions for the Boolean algebra system.
Explain something that need to be followed when applied operators on the element set.
Postulates:

## Slide 2
  A set S is closed with respect to a binary operator if, for every pair of elements of S, the binary operator specifies a rule for obtaining a unique element of S.
Closure
S = { N | 1, 2 , 3 , 4 , 5…… }
B = { +, – }
2 + 3 = 5 where 2, 3, and 5  S
2 – 3 = -1 where 2 and 3 S, -1  S

## Slide 3
  A binary operator * on a set S is said to be commutative whenever
  x * y = y * x for all x, y Î S
Commutative law
S = { N | 1, 2 , 3 , 4 , …… }
B = { +, – }
2 + 3 = 3 + 2 = 5
1 = 3 – 2 ≠ 2 – 3 = -1

## Slide 4
  If * and • are two binary operators on a set S, * is said to be distributive over • whenever
  x * (y • z) = (x * y) • (x * z)
Distributive law
S = { N | 1, 2 , 3 , 4 , …… }
B = { +,  }
3  (2 + 3) = 3  2 + 3  3 = 15
9 = 3 + (2  3) ≠ (3 + 2)  (3 + 3) = 30

## Slide 5
  A set S is said to have an identity element with respect to a binary operation * on S if there exists an element e Î S with the property that
  e * x = x * e = x for every x Î S
Identity law
S = { N | 1, 2 , 3 , 4 , …… }
B = {  }
1  2 = 2  1 = 2
1 is an identity element with respect to a binary operation  on S

## Slide 6
  If * is a binary operator on a set S, for every element x Î S, there exists an element x’ Î S (called the complement of x) such that x * x’ = x’ * x = e
Complement

## Slide 7
  There exist at least two elements x, y Î S such that x ≠ y.
|S| ≥ 2

## Slide 8
Two-valued Boolean Algebra |  | 
A set of elements | A set of operators | A set of postulates
S = {0, 1} | B = {· , +} | Closure
 |  | Commutative law
 |  | Distributive law
 |  | Identity element
 |  | Complement
 |  | ¦S¦ ≥ 2

## Slide 9: Two-valued Boolean Algebra
x | y | x · y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x + y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | x’
0 | 1
1 | 0

## Slide 10
x | y | x · y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x + y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | x’
0 | 1
1 | 0
Postulates | 
Closure | 
Commutative law | 
Distributive law | 
Identity element | 
Complement | 
¦S¦ ≥ 2 | 
Set of elements | Set of operators
S = {0, 1} | B = { +, · }

## Slide 11
Postulates | 
Closure | 
Commutative law | 
Distributive law | 
Identity element | 
Complement | 
¦S¦ ≥ 2 | 
Set of elements | Set of operators
S = {0, 1} | B = { +, · }
x | y | x · y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x + y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | x’
0 | 1
1 | 0

## Slide 12
Postulates | 
Closure | 
Commutative law | 
Distributive law | 
Identity element | 
Complement | 
¦S¦ ≥ 2 | 
  The structure is closed with respect to the operator +.
  The structure is closed with respect to the operator •.
x | y | x · y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x + y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | x’
0 | 1
1 | 0

## Slide 13
Postulates | 
Closure | 
Commutative law | 
Distributive law | 
Identity element | 
Complement | 
¦S¦ ≥ 2 | 
  The element 0 is an identity element with respect to +; that is, x + 0 = 0 + x = x.
  The element 1 is an identity element with respect to •; that is, x • 1 = 1 • x = x.
x | y | x · y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x + y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | x’
0 | 1
1 | 0

## Slide 14
Postulates | 
Closure | 
Commutative law | 
Distributive law | 
Identity element | 
Complement | 
¦S¦ ≥ 2 | 
  The structure is commutative with respect to +; that is, x + y = y + x.
  The structure is commutative with respect to • ; that is, x • y = y • x.
x | y | x · y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x + y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | x’
0 | 1
1 | 0

## Slide 15
x | y | z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
y + z | x · (y + z)
0 | 0
1 | 0
1 | 0
1 | 0
0 | 0
1 | 1
1 | 1
1 | 1
x · y | x · z | (x · y) + (x · z)
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
  The operator • is distributive over +; that is, x • (y + z) = (x • y) + (x • z).

## Slide 16
x | y | z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
y · z | x + (y · z)
0 | 0
0 | 0
0 | 0
1 | 1
0 | 1
0 | 1
0 | 1
1 | 1
x + y | x + z | (x + y) · (x + z)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
  The operator + is distributive over •; that is, x + (y • z) = (x + y) • (x + z).

## Slide 17
Postulates | 
Closure | 
Commutative law | 
Distributive law | 
Identity element | 
Complement | 
¦S¦ ≥ 2 | 
  The operator • is distributive over +; that is, x • (y + z) = (x • y) + (x • z).
  The operator + is distributive over •; that is, x + (y • z) = (x + y) • (x + z).
x | y | x · y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x + y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | x’
0 | 1
1 | 0

## Slide 18
  0 + 0‘ = 0 + 1 = 1; 1 + 1‘ = 1+ 0 = 1
x | y | x + y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
  x + x‘ = 1
x | x’
0 | 1
1 | 0
Complement

## Slide 19
x | y | x · y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
  x · x‘ = 0
x | x’
0 | 1
1 | 0
Complement
  0 ‧ 0‘ = 0 ‧ 1 = 0; 1 ‧ 1‘ = 1 ‧ 0 = 0

## Slide 20
Postulates | 
Closure | 
Commutative law | 
Distributive law | 
Identity element | 
Complement | 
¦S¦ ≥ 2 | 
x | y | x · y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x + y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | x’
0 | 1
1 | 0

## Slide 21
Postulates
1. Closure
2. Identity element
3. Commutative law
4. Distributive law
5. Complement
6. ¦S¦ ≥ 2

## Slide 22
  A set of two elements
  + : OR operation
  ‧ : AND operation
  A complement operator: NOT operation
  Binary logic is a two-valued Boolean algebra

## Slide 23
If an algebraic expression is valid, when interchanging OR and AND operators and replacing 1’s by 0’s and 0’s by 1’s, the resulting expression is also valid.
Duality
The binary operators are interchanged; AND  OR
The identity elements are interchanged; 1  0

## Slide 24
Duality | 
Identity | (a) x + 0 = 0 + x = x
 | (b) x • 1 = 1 • x = x
Commutative | (a) x + y = y + x
 | (b) x • y = y • x
Distributive | (a) x • (y + z) = (x • y) + (x • z)
 | (b) x + (y • z) = (x + y) • (x + z)

## Slide 26
THEOREM 1(a): x + x = x |  |  |  | 
Statement |  |  |  | Postulate
x + x |  |  |  | 

## Slide 27
THEOREM 1(a): x + x = x |  |  |  | 
Statement |  |  |  | Postulate
x + x | = | (x + x) · 1 |  | 2(b)

## Slide 28
THEOREM 1(a): x + x = x |  |  |  | 
Statement |  |  |  | Postulate
x + x | = | (x + x) · 1 |  | 2(b)
 | = | (x + x) · (x + x’) |  | 5(a)

## Slide 29
THEOREM 1(a): x + x = x |  |  |  | 
Statement |  |  |  | Postulate
x + x | = | (x + x) · 1 |  | 2(b)
 | = | (x + x) · (x + x’) |  | 5(a)
 | = | x + x · x’ |  | 4(b)

## Slide 30
THEOREM 1(a): x + x = x |  |  |  | 
Statement |  |  |  | Postulate
x + x | = | (x + x) · 1 |  | 2(b)
 | = | (x + x) · (x + x’) |  | 5(a)
 | = | x + x · x’ |  | 4(b)
 | = | x + 0 |  | 5(b)

## Slide 31
THEOREM 1(a): x + x = x |  |  |  | 
Statement |  |  |  | Postulate
x + x | = | (x + x) · 1 |  | 2(b)
 | = | (x + x) · (x + x’) |  | 5(a)
 | = | x + x · x’ |  | 4(b)
 | = | x + 0 |  | 5(b)
 | = | x |  | 2(a)

## Slide 32
THEOREM 1(b): x · x = x |  |  |  | 
Statement |  |  |  | Postulate
x · x |  |  |  | 

## Slide 33
THEOREM 1(b): x · x = x |  |  |  | 
Statement |  |  |  | Postulate
x · x | = | x · x + 0 |  | 2(a)

## Slide 34
THEOREM 1(b): x · x = x |  |  |  | 
Statement |  |  |  | Postulate
x · x | = | x · x + 0 |  | 2(a)
 | = | x · x + x · x’ |  | 5(b)

## Slide 35
THEOREM 1(b): x · x = x |  |  |  | 
Statement |  |  |  | Postulate
x · x | = | x · x + 0 |  | 2(a)
 | = | x · x + x · x’ |  | 5(b)
 | = | x · (x + x’) |  | 4(a)

## Slide 36
THEOREM 1(b): x · x = x |  |  |  | 
Statement |  |  |  | Postulate
x · x | = | x · x + 0 |  | 2(a)
 | = | x · x + x · x’ |  | 5(b)
 | = | x · (x + x’) |  | 4(a)
 | = | x · 1 |  | 5(a)

## Slide 37
THEOREM 1(b): x · x = x |  |  |  | 
Statement |  |  |  | Postulate
x · x | = | x · x + 0 |  | 2(a)
 | = | x · x + x · x’ |  | 5(b)
 | = | x · (x + x’) |  | 4(a)
 | = | x · 1 |  | 5(a)
 | = | x |  | 2(b)

## Slide 38
THEOREM 2(a): x + 1 = 1 |  |  |  | 
Statement |  |  |  | Postulate
x + 1 |  |  |  | 

## Slide 39
THEOREM 2(a): x + 1 = 1 |  |  |  | 
Statement |  |  |  | Postulate
x + 1 | = | 1 · (x + 1) |  | 2(b)

## Slide 40
THEOREM 2(a): x + 1 = 1 |  |  |  | 
Statement |  |  |  | Postulate
x + 1 | = | 1 · (x + 1) |  | 2(b)
 | = | (x + x’) · (x + 1) |  | 5(a)

## Slide 41
THEOREM 2(a): x + 1 = 1 |  |  |  | 
Statement |  |  |  | Postulate
x + 1 | = | 1 · (x + 1) |  | 2(b)
 | = | (x + x’) · (x + 1) |  | 5(a)
 | = | x + x’ · 1 |  | 4(b)

## Slide 42
THEOREM 2(a): x + 1 = 1 |  |  |  | 
Statement |  |  |  | Postulate
x + 1 | = | 1 · (x + 1) |  | 2(b)
 | = | (x + x’) · (x + 1) |  | 5(a)
 | = | x + x’ · 1 |  | 4(b)
 | = | x + x’ |  | 2(b)

## Slide 43
THEOREM 2(a): x + 1 = 1 |  |  |  | 
Statement |  |  |  | Postulate
x + 1 | = | 1 · (x + 1) |  | 2(b)
 | = | (x + x’) · (x + 1) |  | 5(a)
 | = | x + x’ · 1 |  | 4(b)
 | = | x + x’ |  | 2(b)
 | = | 1 |  | 5(a)

## Slide 44
THEOREM 2(b): x · 0 = 0 |  |  |  | 
Statement |  |  |  | Postulate
x · 0 |  |  |  | 

## Slide 45
THEOREM 2(b): x · 0 = 0 |  |  |  | 
Statement |  |  |  | Postulate
x · 0 | = | 0 + (x · 0) |  | 2(a)

## Slide 46
THEOREM 2(b): x · 0 = 0 |  |  |  | 
Statement |  |  |  | Postulate
x · 0 | = | 0 + (x · 0) |  | 2(a)
 | = | (x · x’) + (x · 0) |  | 5(b)

## Slide 47
THEOREM 2(b): x · 0 = 0 |  |  |  | 
Statement |  |  |  | Postulate
x · 0 | = | 0 + (x · 0) |  | 2(a)
 | = | (x · x’) + (x · 0) |  | 5(b)
 | = | x · (x’ + 0) |  | 4(a)

## Slide 48
THEOREM 2(b): x · 0 = 0 |  |  |  | 
Statement |  |  |  | Postulate
x · 0 | = | 0 + (x · 0) |  | 2(a)
 | = | (x · x’) + (x · 0) |  | 5(b)
 | = | x · (x’ + 0) |  | 4(a)
 | = | x · x’ |  | 2(a)

## Slide 49
THEOREM 2(b): x · 0 = 0 |  |  |  | 
Statement |  |  |  | Postulate
x · 0 | = | 0 + (x · 0) |  | 2(a)
 | = | (x · x’) + (x · 0) |  | 5(b)
 | = | x · (x’ + 0) |  | 4(a)
 | = | x · x’ |  | 2(a)
 | = | 0 |  | 5(b)

## Slide 50
THEOREM 3: involution (x’)’ = x
Postulate 5 defines the complement of x:
x + x’ = 1 and x · x’ = 0
The complement of x’ is x is also (x’)’

## Slide 51
THEOREM 6(a): absorption x + x · y = x |  |  |  | 
Statement |  |  |  | Postulate
x + x · y |  |  |  | 

## Slide 52
THEOREM 6(a): absorption x + x · y = x |  |  |  | 
Statement |  |  |  | Postulate
x + x · y | = | x · 1 + x · y |  | 2(b)

## Slide 53
THEOREM 6(a): absorption x + x · y = x |  |  |  | 
Statement |  |  |  | Postulate
x + x · y | = | x · 1 + x · y |  | 2(b)
 | = | x · (1 + y) |  | 4(a)

## Slide 54
THEOREM 6(a): absorption x + x · y = x |  |  |  | 
Statement |  |  |  | Postulate
x + x · y | = | x · 1 + x · y |  | 2(b)
 | = | x · (1 + y) |  | 4(a)
 | = | x · (y + 1) |  | 3(a)

## Slide 55
THEOREM 6(a): absorption x + x · y = x |  |  |  | 
Statement |  |  |  | Postulate
x + x · y | = | x · 1 + x · y |  | 2(b)
 | = | x · (1 + y) |  | 4(a)
 | = | x · (y + 1) |  | 3(a)
 | = | x · 1 |  | 2(a)

## Slide 56
THEOREM 6(a): absorption x + x · y = x |  |  |  | 
Statement |  |  |  | Postulate
x + x · y | = | x · 1 + x · y |  | 2(b)
 | = | x · (1 + y) |  | 4(a)
 | = | x · (y + 1) |  | 3(a)
 | = | x · 1 |  | 2(a)
 | = | x |  | 2(b)

## Slide 57
THEOREM 6(b): absorption x · (x + y) = x |  |  |  | 
Statement |  |  |  | Postulate
x · (x + y) |  |  |  | 

## Slide 58
THEOREM 6(b): absorption x · (x + y) = x |  |  |  | 
Statement |  |  |  | Postulate
x · (x + y) | = | (x + 0) · (x + y) |  | 2(a)

## Slide 59
THEOREM 6(b): absorption x · (x + y) = x |  |  |  | 
Statement |  |  |  | Postulate
x · (x + y) | = | (x + 0) · (x + y) |  | 2(a)
 | = | x + 0 · y |  | 4(b)

## Slide 60
THEOREM 6(b): absorption x · (x + y) = x |  |  |  | 
Statement |  |  |  | Postulate
x · (x + y) | = | (x + 0) · (x + y) |  | 2(a)
 | = | x + 0 · y |  | 4(b)
 | = | x + y · 0 |  | 3(b)

## Slide 61
THEOREM 6(b): absorption x · (x + y) = x |  |  |  | 
Statement |  |  |  | Postulate
x · (x + y) | = | (x + 0) · (x + y) |  | 2(a)
 | = | x + 0 · y |  | 4(b)
 | = | x + y · 0 |  | 3(b)
 | = | x + 0 |  | 2(b)

## Slide 62
THEOREM 6(b): absorption x · (x + y) = x |  |  |  | 
Statement |  |  |  | Postulate
x · (x + y) | = | (x + 0) · (x + y) |  | 2(a)
 | = | x + 0 · y |  | 4(b)
 | = | x + y · 0 |  | 3(b)
 | = | x + 0 |  | 2(b)
 | = | x |  | 2(a)

## Slide 63
THEOREM 6(a): absorption x + x · y
x | y | x · y | x + x · y
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 

## Slide 64
THEOREM 6(a): absorption x + x · y
x | y | x · y | x + x · y
0 | 0 | 0 | 
0 | 1 | 0 | 
1 | 0 | 0 | 
1 | 1 | 1 | 

## Slide 65
THEOREM 6(a): absorption x + x · y
x | y | x · y | x + x · y
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 1
1 | 1 | 1 | 1

## Slide 66
THEOREM 6(b): absorption x · (x + y) = x
x | y | x + y | x · (x + y)
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 

## Slide 67
THEOREM 6(b): absorption x · (x + y) = x
x | y | x + y | x · (x + y)
0 | 0 | 0 | 
0 | 1 | 1 | 
1 | 0 | 1 | 
1 | 1 | 1 | 

## Slide 68
THEOREM 6(b): absorption x · (x + y) = x
x | y | x + y | x · (x + y)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 1 | 1

## Slide 69
THEOREM 5(a): DeMorgan (x + y)’ = x’ · y’
x | y | x + y | (x + y)’
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
x’ | y’ | x’ · y’

## Slide 70
THEOREM 5(a): DeMorgan (x + y)’ = x’ · y’
x | y | x + y | (x + y)’
0 | 0 | 0 | 
0 | 1 | 1 | 
1 | 0 | 1 | 
1 | 1 | 1 | 
x’ | y’ | x’ · y’

## Slide 71
THEOREM 5(a): DeMorgan (x + y)’ = x’ · y’
x | y | x + y | (x + y)’
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
x’ | y’ | x’ · y’

## Slide 72
THEOREM 5(a): DeMorgan (x + y)’ = x’ · y’
x | y | x + y | (x + y)’
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
x’ | y’ | x’ · y’
1 |  | 
1 |  | 
0 |  | 
0 |  | 

## Slide 73
THEOREM 5(a): DeMorgan (x + y)’ = x’ · y’
x | y | x + y | (x + y)’
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
x’ | y’ | x’ · y’
1 | 1 | 
1 | 0 | 
0 | 1 | 
0 | 0 | 

## Slide 74
THEOREM 5(a): DeMorgan (x + y)’ = x’ · y’
x | y | x + y | (x + y)’
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
x’ | y’ | x’ · y’
1 | 1 | 1
1 | 0 | 0
0 | 1 | 0
0 | 0 | 0

## Slide 75
THEOREM 5(a): DeMorgan (x · y)’ = x’ + y’
x | y | x · y | (x · y)’
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
x’ | y’ | x’ + y’

## Slide 76
THEOREM 5(a): DeMorgan (x · y)’ = x’ + y’
x | y | x · y | (x · y)’
0 | 0 | 0 | 
0 | 1 | 0 | 
1 | 0 | 0 | 
1 | 1 | 1 | 
x’ | y’ | x’ + y’

## Slide 77
THEOREM 5(a): DeMorgan (x · y)’ = x’ + y’
x | y | x · y | (x · y)’
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
x’ | y’ | x’ + y’

## Slide 78
THEOREM 5(a): DeMorgan (x · y)’ = x’ + y’
x | y | x · y | (x · y)’
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
x’ | y’ | x’ + y’
1 |  | 
1 |  | 
0 |  | 
0 |  | 

## Slide 79
THEOREM 5(a): DeMorgan (x · y)’ = x’ + y’
x | y | x · y | (x · y)’
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
x’ | y’ | x’ + y’
1 | 1 | 
1 | 0 | 
0 | 1 | 
0 | 0 | 

## Slide 80
THEOREM 5(a): DeMorgan (x · y)’ = x’ + y’
x | y | x · y | (x · y)’
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
x’ | y’ | x’ + y’
1 | 1 | 1
1 | 0 | 1
0 | 1 | 1
0 | 0 | 0

## Slide 81
The operator precedence for evaluating Boolean expression is:
  Parentheses
  NOT
  AND
  OR

## Slide 82
Using the basic theorems and postulates of Boolean algebra, simplify the following Boolean expression: F = x’y’z + xyz + x’yz + xy’z
Practice Exercise 2.1
F = x’y’z + xyz + x’yz + xy’z

## Slide 83
Using the basic theorems and postulates of Boolean algebra, simplify the following Boolean expression: F = x’y’z + xyz + x’yz + xy’z
Practice Exercise 2.1
F = x’y’z + xyz + x’yz + xy’z
= x’y’z + (x + x’)yz + xy’z

## Slide 84
Using the basic theorems and postulates of Boolean algebra, simplify the following Boolean expression: F = x’y’z + xyz + x’yz + xy’z
Practice Exercise 2.1
F = x’y’z + xyz + x’yz + xy’z
= x’y’z + (x + x’)yz + xy’z
= x’y’z + yz + xy’z

## Slide 85
Using the basic theorems and postulates of Boolean algebra, simplify the following Boolean expression: F = x’y’z + xyz + x’yz + xy’z
Practice Exercise 2.1
F = x’y’z + xyz + x’yz + xy’z
= x’y’z + (x + x’)yz + xy’z
= x’y’z + yz + xy’z
= x’y’z + xy’z + yz

## Slide 86
Using the basic theorems and postulates of Boolean algebra, simplify the following Boolean expression: F = x’y’z + xyz + x’yz + xy’z
Practice Exercise 2.1
F = x’y’z + xyz + x’yz + xy’z
= x’y’z + (x + x’)yz + xy’z
= x’y’z + yz + xy’z
= x’y’z + xy’z + yz
= (x’ + x)y’z + yz

## Slide 87
Using the basic theorems and postulates of Boolean algebra, simplify the following Boolean expression: F = x’y’z + xyz + x’yz + xy’z
Practice Exercise 2.1
F = x’y’z + xyz + x’yz + xy’z
= x’y’z + (x + x’)yz + xy’z
= x’y’z + yz + xy’z
= x’y’z + xy’z + yz
= (x’ + x)y’z + yz
= y’z + yz

## Slide 88
Using the basic theorems and postulates of Boolean algebra, simplify the following Boolean expression: F = x’y’z + xyz + x’yz + xy’z
Practice Exercise 2.1
F = x’y’z + xyz + x’yz + xy’z
= x’y’z + (x + x’)yz + xy’z
= x’y’z + yz + xy’z
= x’y’z + xy’z + yz
= (x’ + x)y’z + yz
= y’z + yz
= (y’ + y)z

## Slide 89
Using the basic theorems and postulates of Boolean algebra, simplify the following Boolean expression: F = x’y’z + xyz + x’yz + xy’z
Practice Exercise 2.1
F = x’y’z + xyz + x’yz + xy’z
= x’y’z + (x + x’)yz + xy’z
= x’y’z + yz + xy’z
= x’y’z + xy’z + yz
= (x’ + x)y’z + yz
= y’z + yz
= (y’ + y)z
= z

## Slide 90
Develop a truth table for the Boolean expression F = x’y’z
Practice Exercise 2.2
x | y | z | F
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 91
Develop a truth table for the Boolean expression F = x’y’z
Practice Exercise 2.2
x | y | z | F
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
= 0’ · 0’ · 0 = 1 · 1 · 0 = 0

## Slide 92
Develop a truth table for the Boolean expression F = x’y’z
Practice Exercise 2.2
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
= 0’ · 0’ · 1 = 1 · 1 · 1 = 1

## Slide 93
Develop a truth table for the Boolean expression F = x’y’z
Practice Exercise 2.2
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
= 0’ · 1’ · 0 = 1 · 0 · 0 = 0

## Slide 94
Develop a truth table for the Boolean expression F = x’y’z
Practice Exercise 2.2
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
= 0’ · 1’ · 1 = 1 · 0 · 1 = 0

## Slide 95
Develop a truth table for the Boolean expression F = x’y’z
Practice Exercise 2.2
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
= 1’ · 0’ · 0 = 0 · 1 · 0 = 0

## Slide 96
Develop a truth table for the Boolean expression F = x’y’z
Practice Exercise 2.2
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
= 1’ · 0’ · 1 = 0 · 1 · 1 = 0

## Slide 97
Develop a truth table for the Boolean expression F = x’y’z
Practice Exercise 2.2
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 
1 | 1 | 1 | 
= 1’ · 1’ · 0 = 0 · 0 · 0 = 0

## Slide 98
Develop a truth table for the Boolean expression F = x’y’z
Practice Exercise 2.2
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 
= 1’ · 1’ · 1 = 0 · 0 · 1 = 0

## Slide 99
Develop a truth table for the Boolean expression F = x’y’z
Practice Exercise 2.2
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
= 1’ · 1’ · 1 = 0 · 0 · 1 = 0

## Slide 100
Logic gates
x | y | x · y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x + y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | x’
0 | 1
1 | 0