## Slide 1: TOPIC 5
Decoder

## Slide 2
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111

## Slide 3
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
A2
A1
A0
D0
D7

## Slide 4
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
A2
A1
A0
D0
D7

## Slide 5
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
A2
A1
A0
D0
D7
3  8
Decoder

## Slide 6
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
A2
A1
A0
D0
D7
3  8
Decoder
3-bit
address bus

## Slide 7
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
A2
A1
A0
D0
D7
3  8
Decoder
3-bit
address bus

## Slide 8
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
A2
A1
A0
D0
D7
3  8
Decoder
3-bit
address bus
1
0
1

## Slide 9
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
A2
A1
A0
D0
D7
3  8
Decoder
3-bit
address bus
1
0
1
0
0
0
0
0
1
0
0

## Slide 10
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
A2
A1
A0
D0
D7
3  8
Decoder
3-bit
address bus
1
0
1
0
0
0
0
0
1
0
0
8-bit data bus

## Slide 11
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
A2
A1
A0
D0
D7
3  8
Decoder
3-bit
address bus
1
0
1
0
0
0
0
0
1
0
0
8-bit data bus
11100101

## Slide 12
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
3  8
Decoder
1
0
1
0
0
0
0
0
1
0
0
8-bit data bus
3-bit
address bus
Memory
A2
A1
A0
D0
D7
11100101

## Slide 13
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
3  8
Decoder
8-bit data bus
3-bit
address bus
Memory
A2
A1
A0
D0
D7

## Slide 14
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
3  8
Decoder
8-bit data bus
3-bit
address bus
Memory
A2
A1
A0
D0
D7
1
1
0

## Slide 15
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
3  8
Decoder
8-bit data bus
3-bit
address bus
Memory
A2
A1
A0
D0
D7
1
1
0
0
0
0
1
0
0
0
0

## Slide 16
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
3  8
Decoder
1
1
0
0
0
0
1
0
0
0
0
8-bit data bus
3-bit
address bus
Memory
A2
A1
A0
D0
D7
10010110

## Slide 17
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
3  8
Decoder
1
1
1
8-bit data bus
3-bit
address bus
Memory
A2
A1
A0
D0
D7

## Slide 18
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
3  8
Decoder
1
1
1
0
0
0
0
0
0
0
1
8-bit data bus
3-bit
address bus
Memory
A2
A1
A0
D0
D7

## Slide 19
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
3  8
Decoder
1
1
1
0
0
0
0
0
0
0
1
8-bit data bus
3-bit
address bus
Memory
A2
A1
A0
D0
D7

## Slide 20
CPU
Contents | Address
10111010 | 000
11110000 | 001
00111100 | 010
10010110 | 011
01100110 | 100
11100101 | 101
11100001 | 110
01100111 | 111
3  8
Decoder
1
1
1
0
0
0
0
0
0
0
1
8-bit data bus
3-bit
address bus
Memory
A2
A1
A0
D0
D7
01100111

## Slide 21
3  8
Decoder
D0
D1
D2
D3
D4
D5
D6
D7
z
y
x

## Slide 22
3  8
Decoder
D0
D1
D2
D3
D4
D5
D6
D7
z
y
x
A 3-to-8 decoder
  3 input variables; up to 23 output lines
  only one output can be active (high) at any time

## Slide 23
3  8
Decoder
D0
D1
D2
D3
D4
D5
D6
D7
z
y
x

## Slide 24
3  8
Decoder
D0
D1
D2
D3
D4
D5
D6
D7
z
y
x
D0 = x’y’z’

## Slide 25
3  8
Decoder
D0
D1
D2
D3
D4
D5
D6
D7
z
y
x
D0 = x’y’z’
D1 = x’y’z

## Slide 26
3  8
Decoder
D0
D1
D2
D3
D4
D5
D6
D7
z
y
x
D0 = x’y’z’
D1 = x’y’z
D2 = x’yz’

## Slide 27
3  8
Decoder
D0
D1
D2
D3
D4
D5
D6
D7
z
y
x
D0 = x’y’z’
D1 = x’y’z
D2 = x’yz’
D3 = x’yz

## Slide 28
3  8
Decoder
D0
D1
D2
D3
D4
D5
D6
D7
z
y
x
D0 = x’y’z’
D1 = x’y’z
D2 = x’yz’
D3 = x’yz
D4 = xy’z’

## Slide 29
3  8
Decoder
D0
D1
D2
D3
D4
D5
D6
D7
z
y
x
D0 = x’y’z’
D1 = x’y’z
D2 = x’yz’
D3 = x’yz
D4 = xy’z’
D5 = xy’z

## Slide 30
3  8
Decoder
D0
D1
D2
D3
D4
D5
D6
D7
z
y
x
D0 = x’y’z’
D1 = x’y’z
D2 = x’yz’
D3 = x’yz
D4 = xy’z’
D5 = xy’z
D6 = xyz’

## Slide 31
3  8
Decoder
D0
D1
D2
D3
D4
D5
D6
D7
z
y
x
D0 = x’y’z’
D1 = x’y’z
D2 = x’yz’
D3 = x’yz
D4 = xy’z’
D5 = xy’z
D6 = xyz’
D7 = xyz

## Slide 33
Combinational logic implementation
  each output = a minterm
  use a decoder and an external OR gate to implement any Boolean function of n input variables

## Slide 34
Full-Adder
    S(x, y, x) = ∑(1, 2, 4, 7)
    C(x, y, z) = ∑(3, 5, 6, 7)

## Slide 35
    S(x, y, x) = ∑(1, 2, 4, 7)
    C(x, y, z) = ∑(3, 5, 6, 7)

## Slide 36
D0
D1
D2
D3
D4
D5
D6
D7
    S(x, y, x) = ∑(1, 2, 4, 7)
    C(x, y, z) = ∑(3, 5, 6, 7)

## Slide 37
D0
D1
D2
D3
D4
D5
D6
D7
    S(x, y, x) = ∑(1, 2, 4, 7)
    C(x, y, z) = ∑(3, 5, 6, 7)

## Slide 38
D0
D1
D2
D3
D4
D5
D6
D7
    S(x, y, x) = ∑(1, 2, 4, 7)
    C(x, y, z) = ∑(3, 5, 6, 7)

## Slide 39
D0
D1
D2
D3
D4
D5
D6
D7
    S(x, y, x) = ∑(1, 2, 4, 7)
    C(x, y, z) = ∑(3, 5, 6, 7)

## Slide 40
D0
D1
D2
D3
D4
D5
D6
D7
    S(x, y, x) = ∑(1, 2, 4, 7)
    C(x, y, z) = ∑(3, 5, 6, 7)

## Slide 42
  A decoder with an enable input
D0
D1
D2
D3
E | A | B | D0 | D1 | D2 | D3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1

## Slide 43
  A decoder with an enable input
D0
D1
D2
D3
E | A | B | D0 | D1 | D2 | D3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
0
0
0
0
0

## Slide 44
  A decoder with an enable input
D0
D1
D2
D3
E | A | B | D0 | D1 | D2 | D3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
1
1
0
0
0
0
0

## Slide 45
  A decoder with an enable input
D0
D1
D2
D3
E | A | B | D0 | D1 | D2 | D3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
1
0
1
0
0
0
1

## Slide 46
  A decoder with an enable input
D0
D1
D2
D3
E | A | B | D0 | D1 | D2 | D3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
1
0
0
1
0
1
0

## Slide 47
  A decoder with an enable input
D0
D1
D2
D3
E | A | B | D0 | D1 | D2 | D3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
1
0
0
0
1
1
1

## Slide 48
  Two 2-to-4 decoder: a 3-to-8 deocder

## Slide 49
  Two 2-to-4 decoder: a 3-to-8 deocder
E | x | y | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 50
  Two 2-to-4 decoder: a 3-to-8 deocder
E | x | y | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1
0
0

## Slide 51
  Two 2-to-4 decoder: a 3-to-8 deocder
E | x | y | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0
1
1

## Slide 52
  Two 3-to-8 decoder: a 4-to-16 deocder

## Slide 53: TOPIC 6
Multiplexer

## Slide 54
+
Operation
CarryIn
Result
CarryOut
a
b
AND
OR
ADD
Function | CarryIn | Op1 | Op0
and | X | 0 | 0
or | X | 0 | 1
add | 0 | 1 | 0
0
1
2

## Slide 55
+
Operation
CarryIn
Result
CarryOut
a
b
AND
OR
ADD
Function | CarryIn | Op1 | Op0
and | X | 0 | 0
or | X | 0 | 1
add | 0 | 1 | 0
0
1
2

## Slide 56
+
Operation
CarryIn
Result
CarryOut
a
b
AND
OR
ADD
Function | CarryIn | Op1 | Op0
and | X | 0 | 0
or | X | 0 | 1
add | 0 | 1 | 0
0
1
2

## Slide 57
+
Operation
CarryIn
Result
CarryOut
a
b
AND
OR
ADD
Function | CarryIn | Op1 | Op0
and | X | 0 | 0
or | X | 0 | 1
add | 0 | 1 | 0
0
1
2

## Slide 58
Multiplexers
  select binary information from one of many input lines and direct it to a single output line.
  2n input lines, n selection lines and one output line
  e.g.: 2-to-1-line multiplexer

## Slide 60
S | I0 | I1 | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 61
 | 00 | 01 | 11 | 10
0 |  |  | 1 | 1
1 |  | 1 | 1 | 
S
I0I1
S | I0 | I1 | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 62
 | 00 | 01 | 11 | 10
0 |  |  | 1 | 1
1 |  | 1 | 1 | 
S
I0I1
S | I0 | I1 | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 63
 | 00 | 01 | 11 | 10
0 |  |  | 1 | 1
1 |  | 1 | 1 | 
S
I0I1
Y = S’ · I0 + S · I1
S | I0 | I1 | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 64
 | 00 | 01 | 11 | 10
0 |  |  | 1 | 1
1 |  | 1 | 1 | 
S
I0I1
Y = S’ · I0 + S · I1
S | I0 | I1 | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 65
  4-to-1-line multiplexer
Y
I0
I1
I2
I3

## Slide 66
S | I0 | I1 | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 67
S | I0 | I1 | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
S | Y
0 | I0
1 | I1

## Slide 68
S | I0 | I1 | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
S | Y
0 | I0
1 | I1
Y = S’ · I0 + S · I1

## Slide 69
S | I0 | I1 | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
S | Y
0 | I0
1 | I1
Y = S’ · I0 + S · I1

## Slide 70
S | I0 | I1 | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
S | Y
0 | I0
1 | I1
Y = 0’ · I0 + 0 · I1 = I0

## Slide 71
S | I0 | I1 | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
S | Y
0 | I0
1 | I1
Y = S’ · I0 + S · I1

## Slide 72
S | I0 | I1 | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
S | Y
0 | I0
1 | I1
Y = 1’ · I0 + 1 · I1 = I1

## Slide 73
  4-to-1-line multiplexer
Y
I0
I1
I2
I3

## Slide 74
  4-to-1-line multiplexer
Y
I0
I1
I2
I3

## Slide 75
  4-to-1-line multiplexer
Y
I0
I1
I2
I3
Y = S1’S0’I0 + S1’S0I1 + S1S0’I2 + S1S0I3

## Slide 76
Y = S1’S0’I0 + S1’S0I1 + S1S0’I2 + S1S0I3

## Slide 77
  MUX: a decoder + an OR gate
  2n-to-1 MUX can implement any Boolean function of n input variable
  a better solution: implement any Boolean function of n+1 input variable
    n of these variables: the selection lines
    the remaining variable: the inputs

## Slide 78
Procedure:
  assign an ordering sequence of the input variable
  the rightmost variable (D) will be used for the input lines
  assign the remaining n-1 variables to the selection lines w.r.t. their corresponding sequence
  construct the truth table
  consider a pair of consecutive minterms starting from m0
  determine the input lines

## Slide 79
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 

## Slide 80
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 

## Slide 81
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 

## Slide 82
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 

## Slide 83
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 

## Slide 84
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 

## Slide 85
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 

## Slide 86
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 

## Slide 87
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 

## Slide 88
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 
0
0
0
1
0

## Slide 89
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 
0
0
1
0
1

## Slide 90
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 
1
0
0
1
1

## Slide 91
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 
1
0
1
0
0

## Slide 92
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 
0
1
0
1
0

## Slide 93
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 
0
1
1
0
0

## Slide 94
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 
1
1
0
1
1

## Slide 95
  An example: F(x, y, z) = (1, 2, 6, 7)
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 
1
1
1
0
1

## Slide 96
Example: F(A, B, C, D) = (1, 3, 4, 11, 12, 13, 14, 15)

## Slide 97
Example: F(A, B, C, D) = (1, 3, 4, 11, 12, 13, 14, 15)

## Slide 98
Example: F(A, B, C, D) = (1, 3, 4, 11, 12, 13, 14, 15)

## Slide 99
Example: F(A, B, C, D) = (1, 3, 4, 11, 12, 13, 14, 15)

## Slide 100
Example: F(A, B, C, D) = (1, 3, 4, 11, 12, 13, 14, 15)

## Slide 101
Example: F(A, B, C, D) = (1, 3, 4, 11, 12, 13, 14, 15)

## Slide 102
Example: F(A, B, C, D) = (1, 3, 4, 11, 12, 13, 14, 15)

## Slide 103
Example: F(A, B, C, D) = (1, 3, 4, 11, 12, 13, 14, 15)

## Slide 104
Example: F(A, B, C, D) = (1, 3, 4, 11, 12, 13, 14, 15)

## Slide 105
Example: F(A, B, C, D) = (1, 3, 4, 11, 12, 13, 14, 15)

## Slide 106
Example: F(A, B, C, D) = (1, 3, 4, 11, 12, 13, 14, 15)

## Slide 107
Example: F(A, B, C, D) = (1, 3, 4, 11, 12, 13, 14, 15)

## Slide 108
  A multiplexer can be constructed with three-state gates
  Output state: 0, 1, and high-impedance (open circuits)

## Slide 109
2-to-1 Multiplexer
0

## Slide 110
2-to-1 Multiplexer
0
1
0

## Slide 111
2-to-1 Multiplexer
0
1
0
X

## Slide 112
2-to-1 Multiplexer
0
1
0
X
Y = A

## Slide 113
2-to-1 Multiplexer
1

## Slide 114
2-to-1 Multiplexer
1
0
1

## Slide 115
2-to-1 Multiplexer
1
0
1
X

## Slide 116
2-to-1 Multiplexer
1
0
1
Y = B
X

## Slide 117
4-to-1 Multiplexer

## Slide 118
4-to-1 Multiplexer
0

## Slide 119
4-to-1 Multiplexer
0
0
0
0
0
X
X
X
X

## Slide 120
4-to-1 Multiplexer
0
0
0
0
0
X
X
X
X
Y =
High-Impedance

## Slide 121
4-to-1 Multiplexer
1
1
0
0
0
X
X
X
0
0

## Slide 122
4-to-1 Multiplexer
1
1
0
0
0
X
X
X
0
0
Y = I0

## Slide 123
4-to-1 Multiplexer
1
0
1
0
0
X
X
X
0
1
Y = I1

## Slide 124
4-to-1 Multiplexer
1
0
0
1
0
X
X
X
1
0
Y = I2

## Slide 125
4-to-1 Multiplexer
1
0
0
0
1
X
X
X
1
1
Y = I3

## Slide 126
Quadruple
2-to-1 Multiplexer
E | S | Y
0 | X | 0
1 | 0 | A
1 | 1 | B

## Slide 127
Quadruple
2-to-1 Multiplexer
E | S | Y
0 | X | 0
1 | 0 | A
1 | 1 | B
0

## Slide 128
Quadruple
2-to-1 Multiplexer
E | S | Y
0 | X | 0
1 | 0 | A
1 | 1 | B
0
0
0
0
0

## Slide 129
Quadruple
2-to-1 Multiplexer
E | S | Y
0 | X | 0
1 | 0 | A
1 | 1 | B
1
0
Y = A
1
0

## Slide 130
Quadruple
2-to-1 Multiplexer
0
Y = B
E | S | Y
0 | X | 0
1 | 0 | A
1 | 1 | B
1
1
1