## Slide 2: Registers and Counters
Chapter 6

## Slide 3: Chapter Objectives
Understand the use, functionality, and modes of operation of registers, shift registers, and universal shift registers.
Know how to properly create the effect of a gated clock.
Understand the structure and functionality of a serial adder circuit.
Understand the behavior of a (a) ripple counter, (b) synchronous counter, (c)ring counter, and (d) Johnson counter.
Be able to write structural and behavioral HDL models of registers, shift registers, universal shift registers, and counters.

## Slide 4: 6.1 Registers
Clocked sequential circuits
  a group of flip-flops and combinational gates
  connected to form a feedback path
  Flip-flops + Combinational gates
  (essential) (optional)
Register:
  a group of flip-flops
  gates that determine how the information is transferred into the register
Counter:
  a register that goes through a predetermined sequence of states

## Slide 5: 6.1 Registers
A n-bit register
  n flip-flops capable of storing n bits of binary information
  4-bit register

## Slide 6
4-bit register with parallel load
load'
load

## Slide 7: 6.2 Shift Registers
Shift register
  a register capable of shifting its binary information in one or both directions
Simplest shift register
1
1
0
1
1
0
1
1
0
1

## Slide 8: Practice Exercise
Practice Exercise 6.1
Objective: Draw the logic diagram of a circuit that suspends the clock action of a D flip-flop without gating its clock. Describe the behavior of the circuit.
Answer:
If Data_gate is 0, Data is transferred to Q with each active edge of clock. If Data_gate is 1, the value of Q is recirculated through the mux-flip-flop path, with the effect that clock appears to be suspended.
Figure PE6.1

## Slide 9
Serial transfer
  Serial transfer
    Information is transferred one bit at a time
    shifts the bits out of the source register into the destination register
  Parallel transfer:
    All the bits of the register are transferred at the same time

## Slide 10
Example: Serial transfer from reg A to reg B

## Slide 11
Example: Serial transfer from reg A to reg B

## Slide 12
Serial addition using D flip-flops
0101
0011
1
1
0
0
1
1010
?001
1
0
1
0
1

## Slide 13
Serial adder using JK flip-flops
    JQ = x y
    KQ = x y = (x + y)
    S = x  y  Q

## Slide 14
  Circuit diagram
    JQ = x y
    KQ = x y = (x + y)
    S = x  y  Q
Ci

## Slide 15: Practice Exercise
Practice Exercise 6.2
Explain why a serial adder is a sequential circuit.
Answer: The circuit uses a flip-flop.

## Slide 16
Universal Shift Register
  Unidirectional shift register
  Bidirectional shift register
  Universal shift register:
    has both direction shifts & parallel load/out capabilities

## Slide 17
Capability of a universal shift register:
  A clear control to clear the register to 0.
  A clock input to synchronize the operations.
  A shift-right control to enable the shift right operation and the serial input and output lines associated w/ the shift right.
  A shift-left control to enable the shift left operation and the serial input and output lines associated w/ the shift left.
  A parallel-load control to enable a parallel transfer and the n parallel input lines associated w/ the parallel transfer.
  n parallel output lines.
  A control state that leaves the information in the register unchanged in the presence of the clock.

## Slide 18
Example: 4-bit universal shift register

## Slide 19
A1
A2
A0

## Slide 20
 Function Table

## Slide 21: 6.3 Ripple Counters
Counter:
  a register that goes through a prescribed sequence of states
  upon the application of input pulses
    Input pulses: may be clock pulses or
    originate from some external source
    The sequence of states: may follow the binary number sequence ( Binary counter) or
    any other sequence of states

## Slide 22
Categories of counters
  Ripple counters
    The flip-flop output transition serves as a source for triggering other flip-flops
     no common clock pulse (not synchronous)
  Synchronous counters:
    The CLK inputs of all flip-flops receive a common clock

## Slide 23
Example: 4-bit binary ripple counter
  Binary count sequence: 4-bit

## Slide 24

10
10

## Slide 25
BCD ripple counter

## Slide 26
The circuit

## Slide 27
Three-decade BCD counter

## Slide 28: 6.4 Synchronous Counters
Sync counter
  A common clock triggers all flip-flops simultaneously
Design procedure
  apply the same procedure of sync seq ckts
  Sync counter is simpler than general sync seq ckts

## Slide 29
4-bit binary counter
C_en A0
C_en A0 A1
C_en A0 A1 A2

## Slide 30
4-bit up/down binary counter
up
down
down A'0
down A'0 A'1
down A'0 A'1 A'2
up A0
up A0 A1

## Slide 31: BCD counters
 Simplified functions:
Table 6.5 State Table for BCD Counter.

## Slide 32
4-bit binary counter w/ parallel load

## Slide 33
async
count load'
load
c_en
c_en A0

## Slide 34
Generate any count sequence
  E.g.: BCD counter  Counter w/ parallel load

## Slide 35: Practice Exercise
Practice Exercise 6.3
How do a ripple counter and a synchronous counter differ in their behavior?
Answer: All of the flip-flops in a synchronous counter are synchronized by receiving a common clock pulse; only the first stage of a ripple counter receives a clock pulse. The stages of a synchronous counter are updated simultaneous by a common clock; the stages of a ripple counter are updated one at a time. A synchronous counter operates faster than a ripple counter.

## Slide 36: 6.5 Other Counters
Counters:
  can be designed to generate any desired sequence of states
Divide-by-N counter (modulo-N counter)
  a counter that goes through a repeated sequence of N states
  The sequence may follow the binary count or may be any other arbitrary sequence

## Slide 37
n flip-flops  2n binary states
Unused states
  states that are not used in specifying the FSM
  may be treated as don’t-care conditions or
  may be assigned specific next states
Self-correcting counter
  Ensure that when a ckt enter one of its unused states, it eventually goes into one of the valid states after one or more clock pulses so it can resume normal operation.
   Analyze the ckt to determine the next state from an
  unused state after it is designed

## Slide 38
An example
  Two unused states: 011 & 111
  The simplified flip-flop input eqs:
  JA = B, KA = B
  JB = C, KB = 1
  JC = B, KC = 1

## Slide 39
  The logic diagram & state diagram of the ckt
The simplified flip-flop input eqs:
JA = B, KA = B
JB = C, KB = 1
JC = B, KC = 1

## Slide 40
Ring counter:
  a circular shift register w/ only one flip-flop being set at any particular time, all others are cleared
  (initial value = 1 0 0 … 0 )
  The single bit is shifted from one flip-flop to the next to produce the sequence of timing signals.

## Slide 41
A 4-bit ring counter
  A2 A2 A1 A0
  1 0 0 0
  0 1 0 0
  0 0 1 0
  0 0 0 1
  1 0 0 0

## Slide 42
Application of counters
  Counters may be used to generate timing signals to control the sequence of operations in a digital system.
Approaches for generation of 2n timing signals
  1. a shift register w/ 2n flip-flops
  2. an n-bit binary counter together w/ an n-to-2n-line decoder

## Slide 44: Johnson counter
Ring counter vs. Switch-tail ring counter
  Ring counter
    a k-bit ring counter circulates a single bit among the flip-flops to provide k distinguishable states.
  Switch-tail ring counter
    is a circular shift register w/ the complement output of the last flip-flop connected to the input of the first flip-flop
    a k-bit switch-tail ring counter will go through a sequence of 2k distinguishable states. (initial value = 0 0 … 0)

## Slide 45
An example: Switch-tail ring counter

## Slide 46
Johnson counter
  a k-bit switch-tail ring counter + 2k decoding gates
  provide outputs for 2k timing signals
    E.g.: 4-bit Johnson counter
  The decoding follows a regular pattern:
    2 inputs per decoding gate

## Slide 47
Disadv. of the switch-tail ring counter
  if it finds itself in an unused state, it will persist to circulate in the invalid states and never find its way to a valid state.
  One correcting procedure: DC = (A + C) B
Summary:
  Johnson counters can be constructed for any # of timing sequences:
  # of flip-flops = 1/2 (the # of timing signals)
  # of decoding gates = # of timing signals
  2-input per gate

## Slide 48: 6.6 HDL for Registers and Counters
 Shift Register
Statement:
A_par <= {MSB_in, A_par [3: 1]}
specifies a concatenation of serial data input for a right shift operation (MSB_in) with bits A_par[3 : 1] of the output data bus.

## Slide 49: HDL Example 6.1 (Universal Shift Register‐Behavioral Model)

## Slide 50: HDL Example 6.1 (Universal Shift Register‐Behavioral Model)

## Slide 51: VHDL Example
註：請修改為
buffer
註：在這兩行之間新增一行，如下：
elsif CLK'event and CLK = '1' then
註：請修改為
Clear_b = '0'
註：請修改為
"0000"
註：這四個依序(由上而下)請修改為
when "00"
when "01"
when "10"
when "11"

## Slide 52: HDL Example 6.2 (Universal Shift Register‐Structural Model)

## Slide 53: HDL Example 6.2 (Universal Shift Register‐Structural Model)

## Slide 54: HDL Example 6.2 (Universal Shift Register‐Structural Model)

## Slide 55: HDL Example 6.2 (Universal Shift Register‐Structural Model)

## Slide 56: VHDL Example
註：請修改為
case sel
註：請修改為
41
註：請修改為
sel
註：請修改為
Std_Logic_Vector

## Slide 57: VHDL Example
註：請修改為
Clr = '1'
註：請修改為
elsif

## Slide 58: VHDL Example
註：請修改為
--
註：請修改為
buffer

## Slide 59: VHDL Example
註：所有標註的中括號請修改為
小括號，例如：[0]  (0)

## Slide 60: HDL Example 6.3 (Synchronous Counter)

## Slide 61: VHDL Example
註：請修改為
Load_vhdl is
註：請修改為
Unsigned
註：請修改為
buffer
註：請修改為
"1111"
註：請修改為
Load_vhdl;
註：請修改為
if Clear_b'event and Clear_b = '0' then A_count <= "0000";
elsif CLK'event and CLK = '1 then
if Load = '1' then A_count <= Data_in;
elsif Count = '1' then A_count <= A_count + "0001";
else A_count <= A_count; -- Redundant statement
end if;

## Slide 62: HDL Example 6.4 (Ripple Counter)

## Slide 63
HDL Example 6.4 (cont.)

## Slide 64: Practice Exercise
Practice Exercise 6.3 – Verilog
The bits of a four-bit ripple counter are labelled A3, A2, A1, and A0. If the flip-flops of the counter are instantiated and interconnected as shown in the text below, the counter fails to function correctly. Find the error in the code
Comp_D_flip_flop F0 (A0, Count, Reset);
Comp_D_flip_flop F1 (A1, A0, Reset);
Comp_D_flip_flop F2 (A2, A3, Reset);
Comp_D_flip_flop F3 (A3, A1, Reset);
Answer: Flip-flops F2 and F3 are not clocked correctly. In F2, replace A3 by A1. In F3, replace A1 by A2.

## Slide 65: VHDL Example
註：請修改為
buffer
註：請修改為
elseif
註：請修改為
endif

## Slide 66: VHDL Example
註：請修改為
Logic;

## Slide 67: VHDL Example
註：這兩行之間請插入一行
end component;

## Slide 68: VHDL Example
註：請修改為
process (); begin
註：請修改為
<= '1'
註：請修改為
<= '0'

## Slide 69
Simulation Output of HDL Example 6.4

## Slide 70
Simulation Output of HDL Example 6.4

## Slide 71: Practice Exercise
Practice Exercise 6.3 – VHDL
The bits of a four-bit ripple counter are labeled A3, A2, A1, and A0. If the flip-flops of the counter are instantiated and interconnected as shown below, the counter fails to function correctly. Find the error in the code
F0: Comp_D_flip_flop port map (Q => A0: out CLK => Count, Reset => Reset);
F1: Comp_D_flip_flop port map (Q => A1: out CLK => A0, Reset => Reset);
F2: Comp_D_flip_flop port map (Q => A2: out CLK => A3, Reset => Reset);
F3: Comp_D_flip_flop port map (Q => A3: out CLK => A1, Reset => Reset);
Answer: Flip-flops F2 and F3 are not clocked correctly. In F2, replace A3 by A1. In F3, replace A1 by A2.

## Slide 72: Web Search Topics
BCD counter
Johnson counter
Ring counter
Sequence detector
Synchronous counter
Switch-tail ring counter
Up–down counter